## Slide 1
CPU

## Slide 6
MUX
SELA
{
MUX
}
SELB
ALU
OPR
R1
R2
R3
R4
R5
R6
R7
Input
3 x 8
decoder
SELD
Load
(7 lines)
Output
A bus
B bus
Clock

## Slide 7: OPERATION OF CONTROL UNIT
The control unit
Directs the information flow through ALU by
- Selecting various Components in the system
- Selecting the Function of ALU
Example: R1 <- R2 + R3
[1] MUX A selector (SELA): BUS A  R2
[2] MUX B selector (SELB): BUS B  R3
[3] ALU operation selector (OPR): ALU to ADD
[4] Decoder destination selector (SELD): R1  Out Bus
Control Word
Encoding of register selection fields
Control
  Binary
  Code SELA SELB SELD
  000 Input Input None
  001 R1 R1 R1
  010 R2 R2 R2
  011 R3 R3 R3
  100 R4 R4 R4
  101 R5 R5 R5
  110 R6 R6 R6
  111 R7 R7 R7
SELA
SELB
SELD
OPR
3
3
3
5

## Slide 8: ALU CONTROL
Encoding of ALU operations
OPR
Select Operation Symbol
00000 Transfer A TSFA
00001 Increment A INCA
00010 ADD A + B ADD
00101 Subtract A - B SUB
00110 Decrement A DECA
01000 AND A and B AND
01010 OR A and B OR
01100 XOR A and B XOR
01110 Complement A COMA
10000 Shift right A SHRA
11000 Shift left A SHLA
Examples of ALU Microoperations
Symbolic Designation
Microoperation SELA SELB SELD OPR Control Word
Control
  R1  R2 - R3 R2 R3 R1 SUB 010 011 001 00101
  R4  R4  R5 R4 R5 R4 OR 100 101 100 01010
  R6  R6 + 1 R6 - R6 INCA 110 000 110 00001
  R7  R1 R1 - R7 TSFA 001 000 111 00000
  Output  R2 R2 - None TSFA 010 000 000 00000
  Output  Input Input - None TSFA 000 000 000 00000
  R4  shl R4 R4 - R4 SHLA 100 000 100 11000
  R5  0 R5 R5 R5 XOR 101 101 101 01100

## Slide 9: REGISTER STACK ORGANIZATION
Register Stack
Push, Pop operations
/* Initially, SP = 0, EMPTY = 1, FULL = 0 */
PUSH
POP
Stack Organization
  SP  SP + 1 DR  M[SP]
  M[SP]  DR SP  SP - 1
  If (SP = 0) then (FULL  1) If (SP = 0) then (EMPTY  1)
  EMPTY  0 FULL  0
Stack
- Very useful feature for nested subroutines, nested loops control
- Also efficient for arithmetic expression evaluation
- Storage which can be accessed in LIFO
- Pointer: SP
- Only PUSH and POP operations are applicable
A
B
C
0
1
2
3
4
63
Address
FULL
EMPTY
SP
DR
Flags
Stack pointer
stack

## Slide 10: MEMORY STACK ORGANIZATION
Stack Organization
- A portion of memory is used as a stack with a
processor register as a stack pointer
- PUSH: SP  SP - 1
  M[SP]  DR
- POP: DR  M[SP]
  SP  SP + 1
- Most computers do not provide hardware to check
stack overflow (full stack) or underflow(empty stack)
Memory with Program, Data,
and Stack Segments
DR
4001
4000
3999
3998
3997
3000
Data
(operands)
Program
(instructions)
1000
PC
AR
SP
stack

## Slide 11: REVERSE POLISH NOTATION
A + B Infix notation
+ A B Prefix or Polish notation
A B + Postfix or reverse Polish notation
- The reverse Polish notation is very suitable for stack manipulation
Evaluation of Arithmetic Expressions
Any arithmetic expression can be expressed in parenthesis-free
Polish notation, including reverse Polish notation
(3 * 4) + (5 * 6)  3 4 * 5 6 * +
Stack Organization
Arithmetic Expressions: A + B
3
3
12
12
12
12
42
4
5
5
6
30
3
4
*
5
6
*
+

## Slide 12: INSTRUCTION FORMAT
OP-code field - specifies the operation to be performed
Address field - designates memory address(es) or a processor register(s)
Mode field - specifies the way the operand or the
effective address is determined
The number of address fields in the instruction format
depends on the internal organization of CPU
- The three most common CPU organizations:
Instruction Format
  Single accumulator organization:
  ADD X /* AC  AC + M[X] */
  General register organization:
  ADD R1, R2, R3 /* R1  R2 + R3 */
  ADD R1, R2 /* R1  R1 + R2 */
  MOV R1, R2 /* R1  R2 */
  ADD R1, X /* R1  R1 + M[X] */
  Stack organization:
  PUSH X /* TOS  M[X] */
  ADD
Instruction Fields

## Slide 13: THREE, AND TWO-ADDRESS INSTRUCTIONS
Three-Address Instructions
Program to evaluate X = (A + B) * (C + D) :
ADD R1, A, B /* R1  M[A] + M[B] */
ADD R2, C, D /* R2  M[C] + M[D] */
MUL X, R1, R2 /* M[X]  R1 * R2 */
- Results in short programs
- Instruction becomes long (many bits)
Two-Address Instructions
Program to evaluate X = (A + B) * (C + D) :
MOV R1, A /* R1  M[A] */
ADD R1, B /* R1  R1 + M[A] */
MOV R2, C /* R2  M[C] */
ADD R2, D /* R2  R2 + M[D] */
MUL R1, R2 /* R1  R1 * R2 */
MOV X, R1 /* M[X]  R1 */
Instruction Format

## Slide 14: ONE, AND ZERO-ADDRESS INSTRUCTIONS
One-Address Instructions
- Use an implied AC register for all data manipulation
- Program to evaluate X = (A + B) * (C + D) :
Instruction Format
LOAD A /* AC  M[A] */
ADD B /* AC  AC + M[B] */
STORE T /* M[T]  AC */
LOAD C /* AC  M[C] */
ADD D /* AC  AC + M[D] */
MUL T /* AC  AC * M[T] */
STORE X /* M[X]  AC */
Zero-Address Instructions
- Can be found in a stack-organized computer
Program to evaluate X = (A + B) * (C + D)
 (REVERSE POLISH NOTATION) A B + C D + *:
PUSH A /* TOS  A */
PUSH B /* TOS  B */
ADD /* TOS  (A + B) */
PUSH C /* TOS  C */
PUSH D /* TOS  D */
ADD /* TOS  (C + D) */
MUL /* TOS  (C + D) * (A + B) */
POP X /* M[X]  TOS */