## Slide 1: Computer System Architecture
Course Code IT2101
Subject Guide: Dr. Aprna Tripathi

## Slide 2: Course Objectives:
The core objective of this course is to describe the general organization and architecture of a computer system.
It covers in detail the description and design of basic computer, functional units, machine instructions, control unit and memory hierarchy design.
It provides a detailed coverage of logic circuits to perform various arithmetic operations and use of pipelining to achieve parallelism to achieve at different levels using hardware and software techniques to yield high-performance processors.

## Slide 3: Course Outcomes:
A student who successfully fulfills the course requirements will be able to:
[2101.1]. Understand the concepts of different combinational and sequential circuits.
[2101.2]. Explain various microoperations and different components of computer organization.
[2101.3]. Describe the operations of control unit and design of various arithmetic circuits.
[2101.4]. Analysis the concepts of I/O organization and memory organization.
[2101.5]. Illustrate the working of pipelining, its interconnection structure and architecture of different processors.

## Slide 4: Student Outcomes (SO):
An ability to apply the knowledge of mathematics, science and computing appropriate to the discipline
An ability to analyze a problem, identify and define the computing requirements appropriate to its solution.
An ability to design, implement and evaluate a system / computer‐based system, process, component or program to meet desired needs

## Slide 5: Assessment Pattern:
At least four assignment
Three quizzes out of which best two will be considered
Quiz can be conducted before announcement
In final assessment
  Assignment- 10
  Quiz – 10

## Slide 6: Syllabus
Basics of Digital Electronics: Codes, Logic Gates, Flip-Flops, Registers, Counters, Multiplexer, De-multiplexer, Encoder, Decoder;
RTL and Micro Operations: Register Transfer, Bus and Memory Transfer, Logic Micro Operations, Shift Micro Operations;
Basic Computer Organization: Complete Computer Description & Design of Basic Computer, Instruction Codes, Computer Instructions, Timing & Control, Instruction Cycles, Memory Reference Instructions, Input/output & Interrupts;
Control Unit: Hardwired vs. Micro Programmed Control Unit, Central Processing Unit, General Register Organization, Stack Organization, Instruction Format, Data Transfer & Manipulation, Program Control, RISC, CISC;
Computer Arithmetic: Addition & Subtraction, Multiplication Algorithms, Division Algorithms;
Input-Output Organization: Peripheral devices, I/O interface, Data Transfer Schemes, Program Control, Interrupt, DMA Transfer, I/O Processor;
Memory Unit: Memory Hierarchy, Processor vs. Memory Speed, High-speed Memory, Cache Memory, Associative Memory, Interleave, Virtual Memory, Memory Management;
Introduction to Parallel Processing: Pipelining, Characteristics of Multiprocessors, Interconnection Structures, Inter-processor Arbitration, Inter-processor Communication & Synchronization;
Case Studies: Case Studies of some Contemporary Advanced Architecture for Processors of Families like Intel, AMD, IBM.

## Slide 7: Text Books:
The main textbook is:
T1. M. Morris Mano, “Computer System Architecture”, Pearson, 3rd Edition Revised, 2017.

## Slide 8: Reference Books:
R1. W. Stallings, “Computer Organization and Architecture –Designing for Performance”, PHI, 2009.
R2. S. Salivahanan & S. Arivazhagan, Digital Circuits and Design, Oxford University Press; Fifth edition, 2018.
R3. David A. Patterson, John L. Hennessy, “Computer Organization and Design: The Hardware/Software Interface”, Morgan Kauffmann, 4th Edition, 2010.
R4. John P. Hayes, “Computer Architecture and Organization”, TMH, 3rd Edition, 1999

## Slide 9: FLIP-FLOPS

## Slide 10: Flip-Flops
No control I/p in latch so I/p S and R can be changed accidently or intentionally therefore this circuit is not suitable for use, so we need to control i/p by which we can decide that when we have to change S and R so that out output Q and Q’ will be stored until we have to use it.
Synchronous circuits change their states only when clock pulses are present.
The operation of the basic latch can be modified, by providing an additional control input that determines, when the state of the circuit is to be changed.
The latch with the additional control input is called the Flip-Flop. The additional control input is clock.
There are four basic types of of flip-flops:
  S-R flip-flops
  J-K flip-flops
  D flip-flops
  T flip-flops

## Slide 11: S-R Flip-Flop
Clk | S | R | Q | Q’
0 | X | X | MEMORY | 
1 | 0 | 0 | MEMORY | 
1 | 0 | 1 | 0 | 1
1 | 1 | 0 | 1 | 0
1 | 1 | 1 | Not Used | 
S | R | Q | Q’
0 | 0 | Not Use | 
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 1 | Memory (as before) | 
NAND-based S R− Latch

## Slide 12: Clk=1
Characteristics table
Qn | Qn+1 | S | R
0 | 0 | 0 | X
0 | 1 | 1 | 0
1 | 0 | 0 | 1
1 | 1 | X | 0
Excitation table

## Slide 13: SR Flip Flop waveform
This is called a positive edge-triggered flip-flop.
The flip-flop output Q changes only after the positive edge of CLK.
The change is based on the flip-flop input values that were present right at the positive edge of the clock signal.

## Slide 14: SR flip – flop
The same can be achieved by using NOR gates.
The figure suggests a structure of RS flip – flop (as R is associated to the output Q), the functionality of SET and RESET remain the same i.e. when S is high, Q is set to 1 and when R is high, Q is reset to 0.
SR flip – flops are very simple but are not widely used in practical circuits because of their illegal state where both S and R are high (S = R = 1).
But they are used in switching circuits as they provide simple switching function (between Set and Reset).
One such application is a Switch de – bounce circuit. The SR flip – flops are used to eliminate mechanical bounce of switches in digital circuits.

## Slide 15: Exercise
(A+C)(AD+AD´)+AC+C=A+C
A+AB=A
A´(A+B)+(B+AA)(A+B´)=A+B
BC+BC´+BA=B
A+A´B+A´B´C+A´B´C´D+A´B´C´D´E=A+B+C+D+E
A(A+B)=A
Notes: (A+C)(AD+AD´)+AC+C=A+C left (A+C right ) left (AD+A acute {D} right ) +AC+C=A+C
4.
A+AB=AA+AB=A
5.
A´(A+B)+(B+AA)(A+B´)=A+Bacute {A} left (A+B right ) + left (B+AA right ) left (A+ acute {B} right ) =A+B
6.
BC+BC´+BA=BBC+B acute {C} +BA=B
7.
A+A´B+A´B´C+A´B´C´D+A´B´C´D´E=A+B+C+D+EA+ acute {A} B+ acute {A} acute {B} C+ acute {A} acute {B} acute {C} D+ acute {A} acute {B} acute {C} acute {D} E=A+B+C+D+E
8.
A(A+B)=A

## Slide 16: D Flip-Flop
The D (delay) flip-flop has only one input called the Delay (D) input and two outputs Q and Q’.
It can be constructed from an S-R flip-flop by inserting an inverter between S and R and assigning the symbol D to the S input.

## Slide 17: J-K Flip-Flop
J-K flip-flop has a similar characteristic as that of an S-R flip-flop.
In addition, the indeterminate condition of the S-R flip-flop is permitted in it.
Inputs J and K behave like inputs S and R to set and reset the flip-flop.
When J = K = 1, the flip-flop output toggles, i.e. switches to its complement state; if Q = 0, it switches to Q =1 and vice versa.

## Slide 18: J-K Flip-Flop

## Slide 19: JK Flip flop waveform and state diagram

## Slide 20: T Flip-Flop
Another basic flip-flop, called the T or trigger or toggle flip-flop, has only a single data (T) input, a clock input and two outputs Q and Q’ .
The T-type flip-flop is obtained from a J-K flip-flop by connecting its J and K inputs together.
The designation T comes from the ability of the flip-flop to “toggle” or complement its state.

## Slide 21: Counters

## Slide 22: Introduction: Counters
Counters are circuits that cycle through a specified number of states.
Two types of counters:
  synchronous (parallel) counters
  asynchronous (ripple) counters
Ripple counters allow some flip-flop outputs to be used as a source of clock for other flip-flops.
Synchronous counters apply the same clock to all flip-flops.

## Slide 23: Types of Counter
Classification
Asynchronous/Ripple counter 2.Synchronous counters
External clock plus applied to one FF All FF receive external clock
Asynchronous counter | Synchronous counter
Flip flops are connected in such a way that the output of first FF derives the clock of next FF | There is no connection between o/p of first FF and clock of next FF
Flips are not clocked simultaneously | Flips are clocked simultaneously
Circuit is simple for more number of state | Circuit become complicated as no of states increased
Speed is slow as clock is propagated through number of stages | Speed is high as clock is given at a same time

## Slide 24: Asynchronous (Ripple) Counters
Asynchronous counters: the flip-flops do not change states at exactly the same time as they do not have a common clock pulse.
Also known as ripple counters, as the input clock pulse “ripples” through the counter – cumulative delay is a drawback.
n flip-flops  a MOD (modulus) 2n counter. (Note: A MOD-x counter cycles through x states.)
Output of the last flip-flop (MSB) divides the input clock frequency by the MOD number of the counter, hence a counter is also a frequency divider.

## Slide 25: Asynchronous (Ripple) Counters
Example: 2-bit ripple binary counter.
Output of one flip-flop is connected to the clock input of the next more-significant flip-flop.
K
J
K
J
HIGH
Q0
Q1
Q0
FF1
FF0
CLK
C
C
Timing diagram
00  01  10  11  00 ...
4
3
2
1
CLK
Q0
Q0
Q1
1
1
1
1
0
0
0
0
0
0

## Slide 26: Asynchronous (Ripple) Counters
Example: 3-bit ripple binary counter.

## Slide 27: Asynchronous (Ripple) Counters
As we can see that initially, the outputs of all the 3 flip-flop is 0.
But as we move further then we see that at the first falling edge of the clock input, QA is 1 while QB and QC are 0, thereby providing decimal equivalent as 0.
Again for the second falling edge of the clock input QB is 1 whereas QA and QC are 0, giving a decimal count 1.

## Slide 28: Asynchronous (Ripple) Counters
Propagation delays in an asynchronous (ripple-clocked) binary counter.
If the accumulated delay is greater than the clock pulse, some counter states may be misrepresented!
4
3
2
1
CLK
Q0
Q1
Q2
tPLH
(CLK to Q0)
tPHL (CLK to Q0)
tPLH (Q0 to Q1)
tPHL (CLK to Q0)
tPHL (Q0 to Q1)
tPLH (Q1 to Q2)

## Slide 29: Asynchronous (Ripple) Counters
Example: 4-bit ripple binary counter (negative-edge triggered).
K
J
K
J
Q1
Q0
FF1
FF0
C
C
K
J
C
FF2
Q2
CLK
HIGH
K
J
C
FF3
Q3
CLK
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
Q0
Q1
Q2
Q3

## Slide 30: Asyn. Counters with MOD no. < 2n
States may be skipped resulting in a truncated sequence.
Technique: force counter to recycle before going through all of the states in the binary sequence.
Example: Given the following circuit, determine the counting sequence (and hence the modulus no.)
K
J
Q
Q
CLK
CLR
K
J
Q
Q
CLK
CLR
K
J
Q
Q
CLK
CLR
C
B
A
B
C
All J, K inputs are 1 (HIGH).

## Slide 31: Asyn. Counters with MOD no. < 2n
Example (cont’d):
K
J
Q
Q
CLK
CLR
K
J
Q
Q
CLK
CLR
K
J
Q
Q
CLK
CLR
C
B
A
B
C
All J, K inputs are 1 (HIGH).
A
B
1
2
C
NAND
Output
1
0
3
4
5
6
7
8
9
10
11
12
Clock
MOD-6 counter produced by clearing (a MOD-8 binary counter) when count of six (110) occurs.

## Slide 32: Asyn. Counters with MOD no. < 2n
Example (cont’d): Counting sequence of circuit (in CBA order).
A
B
C
NAND
Output
1
0
1
2
3
4
5
6
7
8
9
10
11
12
Clock
111
000
001
110
101
100
010
011
Temporary state
Counter is a MOD-6 counter.
0
0
0
1
0
0
0
1
0
1
1
0
0
0
1
1
0
1
0
0
0
1
0
0

## Slide 33: Asyn. Counters with MOD no. < 2n
Exercise: How to construct an asynchronous MOD-5 counter? MOD-7 counter? MOD-12 counter?
Question: The following is a MOD-? counter?
K
J
Q
Q
CLR
C
B
A
C
D
E F
All J = K = 1.
K
J
Q
Q
CLR
K
J
Q
Q
CLR
K
J
Q
Q
CLR
K
J
Q
Q
CLR
K
J
Q
Q
CLR
D
E
F

## Slide 34: Asyn. Counters with MOD no. < 2n
Decade counters (or BCD counters) are counters with 10 states (modulus-10) in their sequence. They are commonly used in daily life (e.g.: utility meters, odometers, etc.).
Design an asynchronous decade counter.
D
CLK
HIGH
K
J
C
CLR
Q
K
J
C
CLR
Q
C
K
J
C
CLR
Q
B
K
J
C
CLR
Q
A
(A.C)'

## Slide 35: Asyn. Counters with MOD no. < 2n
Asynchronous decade/BCD counter (cont’d).
D
C
1
2
B
NAND
output
3
4
5
6
7
8
9
10
Clock
11
A
D
CLK
HIGH
K
J
C
CLR
Q
K
J
C
CLR
Q
C
K
J
C
CLR
Q
B
K
J
C
CLR
Q
A
(A.C)'
0
0
0
0
1
0
0
0
0
1
0
0
1
1
0
0
0
0
1
0
1
0
1
0
0
1
1
0
1
1
1
0
0
0
0
1
1
0
0
1
0
0
0
0

## Slide 36: Asynchronous Down Counters
So far we are dealing with up counters. Down counters, on the other hand, count downward from a maximum value to zero, and repeat.
Example: A 3-bit binary (MOD-23) down counter.
K
J
K
J
Q1
Q0
C
C
K
J
C
Q2
CLK
1
Q
Q'
Q
Q'
Q
Q'
Q
Q'
3-bit binary up counter
3-bit binary down counter
1
K
J
K
J
Q1
Q0
C
C
K
J
C
Q2
CLK
Q
Q'
Q
Q'
Q
Q'
Q
Q'

## Slide 37: Asynchronous Down Counters
Example: A 3-bit binary (MOD-8) down counter.
4
3
2
1
CLK
Q0
Q1
1
1
1
0
0
0
1
0
0
0
8
7
6
5
1
1
0
0
1
0
1
0
Q2
1
1
0
1
1
0
0
0
0
001
000
111
010
011
100
110
101
1
K
J
K
J
Q1
Q0
C
C
K
J
C
Q2
CLK
Q
Q'
Q
Q'
Q
Q'
Q
Q'

## Slide 38: Cascading Asynchronous Counters
Larger asynchronous (ripple) counter can be constructed by cascading smaller ripple counters.
Connect last-stage output of one counter to the clock input of next counter so as to achieve higher-modulus operation.
Example: A modulus-32 ripple counter constructed from a modulus-4 counter and a modulus-8 counter.
K
J
K
J
Q1
Q0
C
C
CLK
Q
Q'
Q
Q'
Q
Q'
K
J
K
J
Q3
Q2
C
C
K
J
C
Q4
Q
Q'
Q
Q'
Q
Q'
Q
Q'
Modulus-4 counter
Modulus-8 counter

## Slide 39: Cascading Asynchronous Counters
Example: A 6-bit binary counter (counts from 0 to 63) constructed from two 3-bit counters.
3-bit
binary counter
3-bit
binary counter
Count pulse
A0 A1 A2
A3 A4 A5

## Slide 40: Cascading Asynchronous Counters
If counter is a not a binary counter, requires additional output.
Example: A modulus-100 counter using two decade counters.
CLK
Decade counter
Q3 Q2 Q1 Q0
C
CTEN
TC
1
Decade counter
Q3 Q2 Q1 Q0
C
CTEN
TC
freq
freq/10
freq/100
TC = 1 when counter recycles to 0000

## Slide 41: Synchronous (Parallel) Counters
Synchronous (parallel) counters: the flip-flops are clocked at the same time by a common clock pulse.
We can design these counters using the sequential logic design process
Example: 2-bit synchronous binary counter (using T flip-flops, or JK flip-flops with identical J,K inputs).
01
00
10
11

## Slide 42: Synchronous (Parallel) Counters
Example: 2-bit synchronous binary counter (using T flip-flops, or JK flip-flops with identical J,K inputs).
TA1 = A0
TA0 = 1
1
K
J
K
J
A1
A0
C
C
CLK
Q
Q'
Q
Q'
Q
Q'

## Slide 43: Synchronous (Parallel) Counters
Example: 3-bit synchronous binary counter (using T flip-flops, or JK flip-flops with identical J, K inputs).
TA2 = A1.A0
A2
A1
A0
1
1
TA1 = A0
TA0 = 1
A2
A1
A0
1
1
1
1
A2
A1
A0
1
1
1
1
1
1
1
1

## Slide 44: Synchronous (Parallel) Counters
Example: 3-bit synchronous binary counter (cont’d).
  TA2 = A1.A0 TA1 = A0 TA0 = 1
1
A2
CP
A1
A0
K
Q
J
K
Q
J
K
Q
J

## Slide 45: Synchronous (Parallel) Counters
Note that in a binary counter, the nth bit (shown underlined) is always complemented whenever
  011…11  100…00
  or 111…11  000…00
Hence, Xn is complemented whenever Xn-1Xn-2 ... X1X0 = 11…11.
As a result, if T flip-flops are used, then TXn = Xn-1 . Xn-2 . ... . X1 . X0

## Slide 46: Synchronous (Parallel) Counters
Example: 4-bit synchronous binary counter.
  TA3 = A2 . A1 . A0
  TA2 = A1 . A0
  TA1 = A0
  TA0 = 1
1
K
J
K
J
A1
A0
C
C
CLK
Q
Q'
Q
Q'
Q
Q'
K
J
A2
C
Q
Q'
K
J
A3
C
Q
Q'
A1.A0
A2.A1.A0

## Slide 47: Synchronous (Parallel) Counters
Example: Synchronous decade/BCD counter.
T0 = 1
T1 = Q3'.Q0
T2 = Q1.Q0
T3 = Q2.Q1.Q0 + Q3.Q0

## Slide 48: Synchronous (Parallel) Counters
Example: Synchronous decade/BCD counter (cont’d).
T0 = 1
T1 = Q3'.Q0
T2 = Q1.Q0
T3 = Q2.Q1.Q0 + Q3.Q0
1
Q1
Q0
CLK
T
C
Q
Q'
Q
Q'
Q2
Q3
T
C
Q
Q'
Q
Q'
T
C
Q
Q'
Q
Q'
T
C
Q
Q'
Q
Q'

## Slide 49: Up/Down Synchronous Counters
Up/down synchronous counter: a bidirectional counter that is capable of counting either up or down.
An input (control) line Up/Down (or simply Up) specifies the direction of counting.
  Up/Down = 1  Count upward
  Up/Down = 0  Count downward

## Slide 50: Up/Down Synchronous Counters
Example: A 3-bit up/down synchronous binary counter.
TQ0 = 1
TQ1 = (Q0.Up) + (Q0'.Up' )
TQ2 = ( Q0.Q1.Up ) + (Q0'. Q1'. Up' )
Up counter
TQ0 = 1
TQ1 = Q0
TQ2 = Q0.Q1
Down counter
TQ0 = 1
TQ1 = Q0’
TQ2 = Q0’.Q1’

## Slide 51: Up/Down Synchronous Counters
Example: A 3-bit up/down synchronous binary counter (cont’d).
TQ0 = 1
TQ1 = (Q0.Up) + (Q0'.Up' )
TQ2 = ( Q0.Q1.Up ) + (Q0'. Q1'. Up' )
1
Q1
Q0
CLK
T
C
Q
Q'
Q
Q'
T
C
Q
Q'
Q
Q'
T
C
Q
Q'
Q
Q'
Up
Q2

## Slide 52: Designing Synchronous Counters
Example: A 3-bit Gray code counter (using JK flip-flops).
100
000
001
101
111
110
011
010

## Slide 53: Designing Synchronous Counters
3-bit Gray code counter: flip-flop inputs.
0
1
00 01 11 10
Q2
Q1Q0
X
X
X
X
1
JQ2 = Q1.Q0'
0
1
00 01 11 10
Q2
Q1Q0
X
X
X
X
1
KQ2 = Q1'.Q0'
0
1
00 01 11 10
Q2
Q1Q0
X
X
X
X
1
JQ1 = Q2'.Q0
0
1
00 01 11 10
Q2
Q1Q0
X
X
X
X
1
KQ1 = Q2.Q0
0
1
00 01 11 10
Q2
Q1Q0
X
X
X
X
1
JQ0 = Q2.Q1 + Q2'.Q1'
= (Q2  Q1)'
1
0
1
00 01 11 10
Q2
Q1Q0
X
X
X
X
1
1
KQ0 = Q2.Q1' + Q2'.Q1
= Q2  Q1

## Slide 54: Designing Synchronous Counters
3-bit Gray code counter: logic diagram.
JQ2 = Q1.Q0' JQ1 = Q2'.Q0 JQ0 = (Q2  Q1)'
KQ2 = Q1'.Q0' KQ1 = Q2.Q0 KQ0 = Q2  Q1
Q1
Q0
CLK
Q2
J
C
Q
Q'
K
J
C
Q
Q'
K
J
C
Q
Q'
K
Q2'
Q0'
Q1'

## Slide 55: Register

## Slide 56: Introduction: Registers
An n-bit register has a group of n flip-flops and some logic gates and is capable of storing n bits of information.
The flip-flops store the information while the gates control when and how new information is transferred into the register.
Some functions of register:
  retrieve data from register
  store/load new data into register (serial or parallel)
  shift the data within register (left or right)

## Slide 57: Simple Registers
No external gates.
Example: A 4-bit register. A new 4-bit data is loaded every clock cycle.
A3
CP
A1
A0
D
Q
D
Q
Q
D
A2
D
Q
I3
I1
I0
I2

## Slide 58: Registers With Parallel Load
Instead of loading the register at every clock pulse, we may want to control when to load.
Loading a register: transfer new information into the register. Requires a load control input.
Parallel loading: all bits are loaded simultaneously.

## Slide 59: Registers With Parallel Load
A0
CLK
D
Q
Load
I0
A1
D
Q
A2
D
Q
A3
D
Q
CLEAR
I1
I2
I3
Load'.A0 + Load. I0

## Slide 61: Using Registers to implement Sequential Circuits
A sequential circuit may consist of a register (memory) and a combinational circuit.
Register
Combin-ational circuit
Clock
Inputs
Outputs
Next-state value
The external inputs and present states of the register determine the next states of the register and the external outputs, through the combinational circuit.
The combinational circuit may be implemented by any of the methods covered in MSI components and Programmable Logic Devices.

## Slide 62: Using Registers to implement Sequential Circuits
Example 1:
  A1+ = S m(4,6) = A1.x'
  A2+ = S m(1,2,5,6) = A2.x' + A2'.x = A2  x
  y = S m(3,7) = A2.x
A1
A2
x
y
A1.x'
A2x

## Slide 63: Using Registers to implement Sequential Circuits
Example 2: Repeat example 1, but use a ROM.
ROM truth table
A1
A2
x
y
8 x 3 ROM

## Slide 64: Shift Registers
Another function of a register, besides storage, is to provide for data movements.
Each stage (flip-flop) in a shift register represents one bit of storage, and the shifting capability of a register permits the movement of data from stage to stage within the register, or into or out of the register upon application of clock pulses.

## Slide 65: Shift Registers
Basic data movement in shift registers (four bits are used for illustration).
Data in
Data out
(a) Serial in/shift right/serial out
Data in
Data out
(b) Serial in/shift left/serial out
Data in
Data out
(c) Parallel in/serial out
Data out
Data in
(d) Serial in/parallel out
Data out
Data in
(e) Parallel in / parallel out
(f) Rotate right
(g) Rotate left

## Slide 66: Serial In/Serial Out Shift Registers
Accepts data serially – one bit at a time – and also produces output serially.
Q0
CLK
D
C
Q
Q1
Q2
Q3
Serial data input
Serial data output
D
C
Q
D
C
Q
D
C
Q

## Slide 67: Serial In/Serial Out Shift Registers
Application: Serial transfer of data from one register to another.
Shift register A
Shift register B
SI
SI
SO
SO
Clock
Shift control
CP
Wordtime
T1
T2
T3
T4
CP
Clock
Shift control

## Slide 68: Serial In/Serial Out Shift Registers
Serial-transfer example.

## Slide 69: Serial In/Parallel Out Shift Registers
Accepts data serially.
Outputs of all stages are available simultaneously.
Q0
CLK
D
C
Q
Q1
D
C
Q
Q2
D
C
Q
Q3
D
C
Q
Data input
D
C
CLK
Data input
Q0
Q1
Q2
Q3
SRG 4
Logic symbol

## Slide 70: Parallel In/Serial Out Shift Registers
Bits are entered simultaneously, but output is serial.
D0
CLK
D
C
Q
D1
D
C
Q
D2
D
C
Q
D3
D
C
Q
Data input
Q0
Q1
Q2
Q3
Serial data out
SHIFT/LOAD
SHIFT.Q0 + SHIFT'.D1

## Slide 71: Parallel In/Serial Out Shift Registers
Bits are entered simultaneously, but output is serial.
Logic symbol
C
CLK
SHIFT/LOAD
D0
D1
D2
D3
SRG 4
Serial data out
Data in

## Slide 72: Parallel In/Parallel Out Shift Registers
Simultaneous input and output of all data bits.
Q0
CLK
D
C
Q
Q1
D
C
Q
Q2
D
C
Q
Q3
D
C
Q
Parallel data inputs
D0
D1
D2
D3
Parallel data outputs

## Slide 73: Bidirectional Shift Registers
Data can be shifted either left or right, using a control line RIGHT/LEFT (or simply RIGHT) to indicate the direction.
CLK
D
C
Q
D
C
Q
D
C
Q
D
C
Q
Q0
Q1
Q2
Q3
RIGHT/LEFT
Serial data in
RIGHT.Q0 + RIGHT'.Q2

## Slide 74: Bidirectional Shift Registers
4-bit bidirectional shift register with parallel load.
CLK
I4
I3
I2
I1
Serial input for shift-right
D
Q
D
Q
D
Q
D
Q
Clear
4x1 MUX
s1
s0
3 2 1 0
4x1 MUX
3 2 1 0
4x1 MUX
3 2 1 0
4x1 MUX
3 2 1 0
A4
A3
A2
A1
Serial input for shift-left
Parallel inputs
Parallel outputs

## Slide 75: Bidirectional Shift Registers
4-bit bidirectional shift register with parallel load.

## Slide 76
Register Transfer and Microoperations

## Slide 77: Register
Basically Register is a collection of individual flip flop connected in numbers to form different size of registers.
Computer registers are designated by capital letters (sometimes followed by numerals) to denote the function of the register
    R1: processor register
    MAR: Memory Address Register (holds an address for a memory unit)
    PC: Program Counter
    IR: Instruction Register
    SR: Status Register
R1

## Slide 78
The individual flip-flops in an n-bit register are numbered in sequence from 0 to n-1 (from the right position toward the left position)
R1
7 6 5 4 3 2 1 0
A block diagram of a register
Register R1
Showing individual bits

## Slide 79
R2
Numbering of bits
Partitioned into two parts
15
0
PC(H)
PC(L)
0
7
8
15
Lower byte
Upper byte
Other ways of drawing the block diagram of a register:

## Slide 80: Microoperation
The operation executed on data stored in registers are called microoperations
Microoperation is an elementary operation performed on the information stored in one or more registers.
Result of Miro operation is also stored in register. It may replace the previous binary information of a register or may be transferred to another register.
Shift, count, clear, load

## Slide 81: Register Transfer Language (RTL)
Register Transfer Language (RTL) : a symbolic notation used to describe the microoperation transfers among registers is called RTL
Language of representing the transfer of data from one register to another register
The term register transfer implies the availability of hardware logic circuit that can perform a stated microoperation and transfer the result of the operation to the same or another register.
A RTL is a system for expressing in symbolic form the microoperation sequence among the register of a digital module

## Slide 82: register
Information transfer from one register to another is designated in symbolic form by mean of a replacement operation is known as Register transfer
R2 ← R1
This statement denotes a transfer of the content of register R1 into register R2
The transfer happens in one clock cycle
The content of the R1 (source) does not change
The content of the R2 (destination) will be lost and replaced by the new data transferred from R1

## Slide 83: Register Transfer
Conditional transfer occurs only under a control condition
A control function is a Boolean variable that is equal to 1 and 0. the control function is included in the statement as
P: R2 ← R1
A binary condition (P equals to 0 or 1) determines when the transfer occurs
The content of R1 is transferred into R2 only if P is 1

## Slide 84: Register Transfer
n
Clock
R1
R2
Control Circuit
Load
t
t+1
Clock
Load
Transfer occurs here
Synchronized with the clock
P
Hardware implementation of a controlled transfer: P: R2 ← R1
Block diagram:
Timing diagram

## Slide 85: Register Transfer
Basic Symbols for Register Transfers |  | 
Symbol | Description | Examples
Letters & numerals | Denotes a register | MAR, R2
Parenthesis ( ) | Denotes a part of a register | R2(0-7), R2(L)
Arrow ← | Denotes transfer of information | R2 ← R1
Comma , | Separates two microoperations | R2 ← R1, R1 ← R2

## Slide 86: Register Transfer Language (RTL)
Digital System: An interconnection of hardware modules that do a certain task on the information.
Modules are constructed from digital component as register, decoder, counter…
Registers + Operations performed on the data stored in them = Digital Module
Modules are interconnected with common data and control paths to form a digital computer system

## Slide 87: Register Transfer Language
The internal hardware organization of a digital computer is defined by specifying:
    The set of registers it contains and their function
    The sequence of microoperations performed on the binary information stored in the registers
    The control that initiates the sequence of microoperations
Registers + Microoperations Hardware + Control Functions = Digital Computer

## Slide 88: Bus and Memory Transfers
A typical digital computer has many registers, and path must be provided to transfer information from one register to another.
The number of wires will be excessive if separate lines are used between each register and all other registers in the system
2 register 4 bit require 4 wire. 3 register 4 bit require 12 wire

## Slide 89: Bus and Memory Transfers
3 2 1 0
Register D
D3 D2 D1 D0
3 2 1 0
Register C
C3 C2 C1 C0
3 2 1 0
Register B
B3 B2 B1 B0
3 2 1 0
Register A
A3 A2 A1 A0
D3 C3 B3 A3
S0
S1
MUX3
3 2 1 0
D2 C2 B2 A2
S0
S1
MUX2
3 2 1 0
D1 C1 B1 A1
S0
S1
MUX1
3 2 1 0
D0 C0 B0 A0
S0
S1
MUX0
3 2 1 0
4-Line Common Bus
Register A
Register B
Register C
Register D
Bus lines

## Slide 90: Bus and Memory Transfers
The transfer of information from a bus into one of many destination registers is done:
  By connecting the bus lines to the inputs of all destination registers and then:
  activating the load control of the particular destination register selected
We write: R2 ← C to symbolize that the content of register C is loaded into the register R2 using the common system bus
It is equivalent to: BUS ←C, (select C)
R2 ←BUS (Load R2)

## Slide 91: Bus and Memory Transfers: Three State Bus Buffers
Buffer is having two state input and output. Whatever we give input we get the same output with some delay.
A three-state gate is a digital circuit that exhibits three states.
Two of the states are signals equivalent to logic 1 and 0 as in a conventional gate.
The third state is a high-impedance state which behave like an open circuit, which means that the output is disconnected and does not have logic significance.
A bus system can be constructed with three-state
buffer gates instead of multiplexers
Normal input A
Control input C
Three-State Buffer
Output B

## Slide 92: Bus and Memory Transfers: Three-State Bus Buffers
A
C=1
B
A
B
A
C=0
B
A
B
Buffer
Open Circuit

## Slide 93
The control input determine the output state. When the control input C is equal to 1, the output is enabled and the gate behaves like any conventional buffer, with the output equal to the normal input.
When the control input C is 0, the output is disabled and the gate goes to a high-impedance state, regardless of the value in the normal input.

## Slide 94: Bus and Memory Transfers: Three-State Bus Buffer
2×4 Decoder
Select
Enable
0
1
2
3
S1
S0
E
Bus line for bit 0
A0
B0
C0
D0
Bus line with three-state buffer (replaces MUX0 in the previous diagram)

## Slide 95
The microoperations most often encountered in digital computers are classified into four categories:
  Register transfer microoperations
  Arithmetic microoperations (on numeric data stored in the registers)
  Logic microoperations (bit manipulations on non-numeric data)
  Shift microoperations

## Slide 96: Arithmetic Microoperations cont.
Arithmetic microoperation perform arithmetic operation on numeric data stored in registers.
The basic arithmetic microoperations are: addition, subtraction, increment, decrement
Addition Microoperation:
R3 ←R1+R2
Subtraction Microoperation:
R3 ←R1-R2 or :
R3 ←R1+R2+1 (2’s complement)

## Slide 97: Arithmetic Microoperations cont.
One’s Complement Microoperation:
R2 ←R2
Two’s Complement Microoperation:
R2 ←R2+1
Increment Microoperation:
R2 ←R2+1
Decrement Microoperation:
R2 ←R2-1

## Slide 98: Arithmetic Microoperations Binary Adder
FA
FA
FA
FA
C0
A0
B0
S0
A1
B1
S1
A2
B2
S2
A3
B3
S3
C1
C2
C3
C4
4-bit binary adder (connection of FAs)

## Slide 99: Arithmetic Microoperations Binary Adder-Subtractor
FA
FA
FA
FA
C0
A0
B0
S0
A1
B1
S1
A2
B2
S2
A3
B3
S3
C1
C2
C3
C4
4-bit adder-subtractor
M

## Slide 100: Arithmetic Microoperations Binary Adder-Subtractor
For unsigned numbers, this gives A – B if A≥B or the 2’s complement of (B – A) if A < B
(example: 3 – 5 = -2= 1110)
For signed numbers, the result is A – B provided that there is no overflow. (example : -3 – 5= -8) 1101
1011 +
ـــــــــــــــــــــــــــ
1000
C3
C4
V =
1, if overflow
0, if no overflow
Overflow detector for signed numbers

## Slide 101: Arithmetic Microoperations Binary Incrementor
C
S
x
y
HA
C
S
x
y
HA
C
S
x
y
HA
C
S
x
y
HA
S0
S1
S2
S3
C4
1
A0
A1
A2
A3
4-bit Binary Incrementer

## Slide 102: Arithmetic Microoperations Binary Incrementor
Binary Incrementer can also be implemented using a counter
A binary decrementer can be implemented by adding 1111 to the desired register each time!

## Slide 103: Arithmetic Microoperations Arithmetic Circuit
This circuit performs seven distinct arithmetic operations and the basic component of it is the parallel adder
The output of the binary adder is calculated from the following arithmetic sum:
    D = A + Y + Cin

## Slide 104: Arithmetic Microoperations Arithmetic Circuit
B0
3 2 1 0 S1 S0
4×1 MUX
FA
FA
FA
FA
Cin
D0
D1
D2
D3
C1
C2
C3
Cout
B0
1
0
S1
S0
B1
3 2 1 0 S1 S0
4×1 MUX
B1
1
0
S1
S0
B2
3 2 1 0 S1 S0
4×1 MUX
B2
1
0
S1
S0
B3
3 2 1 0 S1 S0
4×1 MUX
B3
1
0
S1
S0
A0
A1
A2
A3
4-bit Arithmetic Circuit
X0
Y0
X1
Y1
X2
Y2
X3
Y3
Figure A

## Slide 106: Logic Microoperations: The four basic microoperations
OR Microoperation
Symbol: , +
Gate:
Example: 1001102  10101102 = 11101102
P+Q: R1←R2+R3, R4←R5 R6

## Slide 107: Logic Microoperations The four basic microoperations
AND Microoperation
Symbol: 
Gate:
Example: 1001102  10101102 = 00001102

## Slide 108: Logic Microoperations The four basic microoperations cont.
Complement (NOT) Microoperation
Symbol: 
Gate:
Example: 10101102 = 01010012

## Slide 109: Logic Microoperations The four basic microoperations
XOR (Exclusive-OR) Microoperation
Symbol: 
Gate:
Example: 1001102  10101102 = 11100002

## Slide 110: Logic Microoperations Other Logic Microoperations
Selective-set Operation
The selective set operation sets to 1 the bits in register A where there are corresponding 1’s in register B
It does not affect bit positions that have 0’s in B.
Example: A: 0100 B: 1100
A OR B ------1100

## Slide 111: Logic Microoperations Other Logic Microoperations
Selective-complement (toggling) Operation
The selective complement operation complement bits in A where there are corresponding 1’s in B
It does not affect bit position that have 0’s in B
The Ex-OR microoperation can be used
A(before)---1010 B----1100
A(After)---0100

## Slide 112: Logic Microoperations Other Logic Microoperations
Insert Operation
Step1: mask the desired bits
Step2: OR them with the desired value
Example: suppose R1 = 0110 1010, and we desire to replace the leftmost 4 bits (0110) with 1001 then:
  Step1: 0110 1010  0000 1111
  Step2: 0000 1010  1001 0000
 R1 = 1001 1010

## Slide 113: Logic Microoperations Other Logic Microoperations cont.
NAND Microoperation
Symbols:  and 
Gate:
Example: 1001102  10101102 = 11110012

## Slide 114: Logic Microoperations Other Logic Microoperations cont.
NOR Microoperation
Symbols:  and 
Gate:
Example: 1001102  10101102 = 00010012

## Slide 115: Logic Microoperations Other Logic Microoperations
Set (Preset) Microoperation
Force all bits into 1’s by ORing them with a value in which all its bits are being assigned to logic-1
Example: 1001102  1111112 = 1111112
Clear (Reset) Microoperation
Force all bits into 0’s by ANDing them with a value in which all its bits are being assigned to logic-0
Example: 1001102  0000002 = 0000002

## Slide 116: Logic Microoperations Hardware Implementation
The hardware implementation of logic microoperations requires that logic gates be inserted for each bit or pair of bits in the registers to perform the required logic function
Most computers use only four (AND, OR, XOR, and NOT) from which all others can be derived.

## Slide 117: Logic Microoperations Hardware Implementation cont.
S1 | S0 | Output | Operation
0 | 0 | E = A  B | XOR
0 | 1 | E = A  B | OR
1 | 0 | E = A  B | AND
1 | 1 | E = A | Complement
S1
S0
0
1
2
3
4×1 MUX
Ei
Ai
Bi
This is for one bit i
Figure B

## Slide 118: Shift Microoperations
Used for serial transfer of data
Also used in conjunction with arithmetic, logic, and other data-processing operations
The contents of the register can be shifted to the left or to the right
As being shifted, the first flip-flop receives its binary information from the serial input
Three types of shift: Logical, Circular, and Arithmetic

## Slide 119: Shift Microoperations cont.
r0
r1
r3
rn-1
r0
r1
r2
r3
rn-1
Shift Right
Shift Left
Serial Input
Serial Output
Serial Output
Serial Input
Determines the “shift” type
r2
**Note that the bit ri is the bit at position (i) of the register

## Slide 120: Shift Microoperations: Logical Shifts
Logical Shift Left
?
0
r0
r1
r2
r3
rn-1
A logical shift is one that transfer 0 through the serial input.
shl – logical shift left
1 1 0 1
1 0 1 0
Shr logical shift right
1 1 0 1
0 1 1 0

## Slide 121: Shift Microoperations: Circular Shifts (Rotate Operation)
Circular Shift Left
r0
r1
r2
r3
rn-1
A circular Shift circulates the bits of the register around the two ends without loss of information
This is accomplished by connecting the serial output of the shift register to its serial input
cil circular shift left
1 1 0 1
1 0 1 1
cir circular shift right
1 1 0 1
1 1 1 0

## Slide 122: Shift Microoperations Arithmetic Shifts
Shifts a signed binary number to the left or right
An arithmetic shift-left multiplies a signed binary number by 2: ashl (00100): 01000
An arithmetic shift-right divides the number by 2
ashr (00100) : 00010
An overflow may occur in arithmetic shift-left, and occurs when the sign bit is changed (sign reversal)

## Slide 123: Shift Microoperations Arithmetic Shifts cont.
An overflow flip-flop Vs can be used to detect an arithmetic shift-left overflow
Vs = Rn-1  Rn-2
Rn-2
Vs=
Rn-1
1  overflow
0  no overflow

## Slide 124
Assume R1=11001110, then:
  Arithmetic shift right once :
  Arithmetic shift right twice
  Arithmetic shift left once
  Arithmetic shift left twice :
  Logical shift right once :
  Logical shift left once :
  Circular shift right once :
  Circular shift left once :
Example:

## Slide 125: Shift Microoperations cont.
Example: Assume R1=11001110, then:
  Arithmetic shift right once : R1 = 11100111
  Arithmetic shift right twice : R1 = 11110011
  Arithmetic shift left once : R1 = 10011100
  Arithmetic shift left twice : R1 = 00111000
  Logical shift right once : R1 = 01100111
  Logical shift left once : R1 = 10011100
  Circular shift right once : R1 = 01100111
  Circular shift left once : R1 = 10011101

## Slide 126: Shift Microoperations Hardware Implementation cont.
A possible choice for a shift unit would be a bidirectional shift register with parallel load.
Has drawbacks:
  Needs two pulses (the clock and the shift signal pulse)
  Not efficient in a processor unit where multiple number of registers share a common bus
It is more efficient to implement the shift operation with a combinational circuit

## Slide 128: Arithmetic Logic Shift Unit
Instead of having individual registers performing the microoperations directly, computer systems employ a number of storage registers connected to a common operational unit called an Arithmetic Logic Unit (ALU)

## Slide 129: Arithmetic Logic Shift Unit cont.
0
1
2
3
S3
S2
S1
S0
Bi
Ai
Ai+1
Ai-1
Select
4×1 MUX
Ci
Ci+1
One stage of arithmetic circuit (Fig.A)
One stage of logic circuit (Fig.B)
Di
Ei
Fi
shr
shl
One stage of ALU