## Slide 1: INVENTORY MANAGEMENT

## Slide 2: Introduction
The term inventory means the value or amount of materials or resource on hand. It includes raw material, work-in-process, finished goods & stores & spares.
Inventory Control is the process by which inventory is measured and regulated according to predetermined norms such as economic lot size for order or production, safety stock, minimum level, maximum level, order level etc.
Inventory control pertains primarily to the administration of established policies, systems & procedures in order to reduce the inventory cost.

## Slide 3
To meet unforeseen future demand due to variation in forecast figures and actual figures.
To average out demand fluctuations due to seasonal or cyclic variations.
To meet the customer requirement timely, effectively, efficiently, smoothly and satisfactorily.
To smoothen the production process.
To facilitate intermittent production of several products on the same facility.
To gain economy of production or purchase in lots.
OBJECTIVES OF INVENTORY CONTROL

## Slide 4
To reduce loss due to changes in prices of inventory items.
To meet the time lag for transportation of goods.
To meet the technological constraints of production/process.
To balance various costs of inventory such as order cost or set up cost and inventory carrying cost.
To balance the stock out cost/opportunity cost due to loss of sales against the costs of inventory.
To minimize losses due to deterioration, obsolescence, damage, pilferage etc.
To stabilize employment and improve lab our relations by inventory of human resources and machine efforts.

## Slide 5
Minimum Level– It is the minimum stock to be maintained for smooth production.
Maximum Level – It is the level of stock, beyond which a firm should not maintain the stock.
Reorder Level –The stock level at which an order should be placed.
Safety Stock – Stock for usage at normal rate during the extension of lead time.
Reserve Stock - Excess usage requirement during normal lead time.
Buffer Stock – Normal lead time consumption.
Important Terms

## Slide 6: Inventory Costs
Carrying cost
cost of holding an item in inventory
Ordering cost
cost of replenishing inventory

## Slide 7: Inventory Control Systems
Continuous system (fixed-order-quantity)
constant amount ordered when inventory declines to predetermined level
  order placed for variable amount after fixed passage of time
Periodic system
(fixed-time-period)

## Slide 8: Assumptions of Basic EOQ Model
Demand is known, constant, and independent
Lead time is known and constant
Order quantity received is instantaneous and complete
No shortage is allowed

## Slide 9: Inventory Order Cycle
Demand rate
Time
Lead
time
Lead
time
Order Order placedreceipt
Order Order placed receipt
Inventory Level
Reorder point, R
Order quantity, Q
0

## Slide 10: EOQ Cost Model
Co - cost of placing order
Cc - annual per-unit carrying cost
D - annual demand
Q - order quantity
Annual ordering cost =
Annual carrying cost =
Total cost =
CoD Q
CcQ
2
CoD CcQ Q + 2

## Slide 11
Q2
2
Q
0 =
+ Cc
2
Qopt =
2CoD
Cc
Proving equality of costs at optimal point
=
CoD CcQ Q 2
Q2
=
2CoD
C
c
Qopt =
2CoD
Cc
Deriving Qopt
CoD CcQ
TC = Q + 2
TC =- CoD + Cc
- C0D
Q2
EOQ Cost Model

## Slide 12: EOQ Cost Model (cont.)
Order Quantity, Q
Annual
cost ($)
Total Cost
Carrying Cost =
CcQ
2
Slope = 0
Minimum total cost
Optimal order
Qopt
Ordering Cost =
CoD
Q

## Slide 13: Reorder Point
Level of inventory at which a new order is placed
R = dL
d = demand rate per period
L = lead time
where